	Linear source
in palette	| vectorized |

in diagram
The unit is vectorized and generates the output value calculated as per the formula: / y(t) = a + b cdot t , / where a,~b are for coefficients, y(t) for output signal, t is for current simulation time given in seconds. / Unit properties: / Free term – coefficient a . / Coefficient at t – coefficient b . / The properties can be vectors vec {a}=left [ a_1 , a_2 , ... a_n right ] and vec {b}=left [ b_1 , b_2 , ... b_n right ] , the dimensions of which shall be the same; in this case the vector will also be at the output: / vec{y}(t) = vec{a} + vec{b} cdot t, ~"or" newline y_i(t) = a_i + b_i cdot t, ~ i = 1...n. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Free term [2] / Coefficient at t [5] / Named definition of properties: / Name Value / Free term [a1] / Coefficient at t [b1] / Mixed definition of properties: / Name Value / Free term [a1] / Coefficient at t [5] / Vector definition of properties: / Name Value / Free term [1,1,4,2] / Coefficient at t [2,3,b3,b4] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.