	Exponent
in palette	| vectorized |

in diagram
The unit generates the output value calculated as per the formula: / y(t) = a cdot e^{b cdot t + c} , / where a,~b,~c are for exponential relation coefficients, y(t) is for output signal, scalar or vector, t is for current simulation time given in seconds. / Properties: / Amplification coefficient – coefficient a . / Inverse time constant – coefficient b . / Offset – coefficient c . / The properties can be vectors vec {a}= left [ a_{1} , a_{2} , ... a_{n} right ] , vec {b}= left [ b_{1} , b_{2} , ... b_{n} right ] and vec {c}= left [ c_{1} , c_{2} , ... c_{n} right ] , the dimensions of which shall be the same, in this case the vector will be at the output: / y_i(t) = a_i cdot e^ left ( b_i cdot t + c_i right ) ~=~ a_i cdot exp left ( b_i cdot t + c_i right ),~i=1...n. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Amplification coefficient [2.3] / Inverse time constant [1] / Offset [4] / Named definition of properties: / Name Value / Amplification coefficient [a1] / Inverse time constant [b2] / Offset [c1] / Mixed definition of properties: / Name Value / Amplification coefficient [a1] / Inverse time constant [2] / Offset [0] / Vector definition of properties: / Name Value / Amplification coefficient [2,5] / Inverse time constant [1,1.1] / Offset [2,0] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.