	Hyperbola
in palette	| vectorized |

in diagram
The unit generates the output value calculated as per the formula: / y(t) = k over {%epsilon + t} , / where k, %epsilon are for coefficients, y(t) is for output signal, scalar or vector, t is for current simulation time given in seconds. / Properties: / Numerator - coefficient k . / Minimum value of denominator – coefficient %epsilon . / The properties can be vectors vec {k}= left [ k_{1} , k_{2} , ... k_{n} right ] , vec {%epsilon}= left [ %epsilon_{1} , %epsilon_{2} , ... %epsilon_{n} right ] , the dimensions of which shall be the same, in this case the vector will be at the output: / y_i(t) = k_i over {%epsilon_i + t} , ~ i=1...n. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Numerator [5.3] / Minimum value of denominator [0.01] / Named definition of properties: / Name Value / Numerator [k1] / Minimum value of denominator [eps] / Mixed definition of properties: / Name Value / Numerator [k1] / Minimum value of denominator [0.1] / Vector definition of properties: / Name Value / Numerator [2,2] / Minimum value of denominator [0.01,0.02] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.