	PWL
in palette	| vectorized |

in diagram
The unit generates a random piecewise linear output signal, which is the superposition of linear effects, at the output. / Properties: / Time – t – time marks array, in seconds. / Value of function – y – value array for output signal. / The properties are matrices where the vector of times or values for a certain output vector element is defined in every line. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Time [0,50,80,100] / Value of function [0,5,4,1] / Named definition of properties: / Name Value / Time [t1,t2,t3,t4,t5,t6] / Value of function [y1,y2,y3,y4,y5,y6] / Mixed definition of properties: / Name Value / Time [0,t2,100,200,250,1000] / Value of function [y1,y2,y3,y4,y5,y6] / Vector definition of properties: / Name Value / Time [[t1,t2,t3,t4,t5,t6],[t1,t2,t3,t4,t5,t6]] / Value of function [[y1,y2,y3,y4,y5,y6],[1,2.5,3,4,3,1]] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.