	Meander
in palette

in diagram
The unit generates an output signal consisting of uniform rectangular pulses with preset time and amplitude parameters. / Properties: / The 1st semi-period duration – is the time of the unit generates the first semi-period at its output. / The value of the 1st semi-period – is the output signal delivered by the unit during the first semi-period. / The 2nd semi-period duration – is the time of the unit generates the second semi-period at its output. / The value of the 2nd semi-period – is the output signal delivered by the unit during the second semi-period.