	Demultiplexor
in palette

in diagram
The unit is vectorized and implements “the splitting” of a vector input signal to individual output signals. The outputs can be both scalar and vector (“multi-core”) signals. / This unit by default demultiplex a “two-core” input vector signal to scalar signals: / matrix {{y_1 \( t \) = u_1,1 \( t \) ,} ## {y_2 \( t \) = u_1,2 \( t \) ,}} / where y_{1}(t),~y_{2}(t) – are the first and the second unit output scalar signals; / u_{1,1}(t),~u_{1,2}(t) – are the 1st and 2nd elements of input vector signal; / Properties: / Output dimensionality array – is an array of integers indicating dimensions of vectors for every output signals of the unit.