	Pack Matrix
in palette	| vectorized |

in diagram
The unit implements transformation of a number of input vector signals into one vector output signal in accordance with the algorithm: / u(t) = left [ stack{ alignl u_1(t) = [u_11(t),... u_1N(t)] # alignl u_2(t) = [u_21(t),... u_2N(t)] # alignl . . . . . . . . . . . . . . . . . . # alignl u_M(t) = [u_M1(t),... u_MN(t)] } right none ~ dlrarrow ~ left [ stack{ alignl u_11(t),... u_1N(t) # alignl u_21(t),... u_2N(t) # alignl . . . . . . . . . . . . . . . . . . # alignl u_M1(t),... u_MN(t) } right ] ~drarrow~ / y(t) = left [ stack{ alignl u_11(t),... u_1N(t),u_21(t),... u_2N(t),u_M1(t),... u_MN(t) # alignl "or" # alignl u_11(t),... u_M1(t),u_12(t),... u_M2(t),u_1N(t),... u_MN(t) } right ] / or / u(t) = left [ stack{ alignl u_1(t) = [u_11(t),... u_M1(t)] # alignl u_2(t) = [u_12(t),... u_M2(t)] # alignl . . . . . . . . . . . . . . . . . . # alignl u_N(t) = [u_1N(t),... u_MN(t)] } right none ~ dlrarrow ~ left [ stack{ alignl u_11(t),... u_M1(t) # alignl u_12(t),... u_M2(t) # alignl . . . . . . . . . . . . . . . . . . # alignl u_1N(t),... u_MN(t) } right ] ~drarrow~ / y(t) = left [ stack{ alignl u_11(t),... u_1N(t),u_21(t),... u_2N(t),u_M1(t),... u_MN(t) # alignl "or" # alignl u_11(t),... u_M1(t),u_12(t),... u_M2(t),u_1N(t),... u_MN(t) } right ] / where y(t) is for vector output signal, u_i(t) is for vector input signals. / Input vectors u_i(t) interpolated as matrix lines and columns with the size [N times M] are transformed into one vector output y(t) (depending on packing variant: by lines or by columns). / Properties: / Number of lines in matrix – number M . / Number of columns in matrix – number N . / Matrix is extracted by – “unpacking” variant for matrix of input signals (by lines or by columns). / Pack matrix by – packing variant for output signal (by lines or by columns). / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Number of lines in matrix [2] / Number of columns in matrix [3] / Matrix is extracted by Lines / Pack matrix by Lines / Named definition of properties: / Name Value / Number of lines in matrix [ny] / Number of columns in matrix [nx] / Matrix is extracted by Lines / Pack matrix by Lines / Mixed definition of properties: / Name Value / Number of lines in matrix [ny] / Number of columns in matrix [5] / Matrix is extracted by Lines / Pack matrix by Lines / Notes: / By default the unit packs two “double-cored” input signals in a matrix with the size [2х2]. In this case input signals are perceived as matrix lines and matrix is packed by its lines. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.