	Integrator
in palette

in diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows: / {{d y}_i \( t \)} over {d t} =k_i cdot u_i \( t \) , / where u_i(t) is the i-th element of input signal to the unit, k_i is an element of the amplification factors vector, y_i \( t \) is for an element of the unit output signal. / In case of zero initial conditions the dynamics of the unit can be represented via the following transfer function: / W \( s \) =k over s (integrator), / that is why the pictogram of the unit has the view of a transfer function of ideal integrating factor. / The dimensions of input, output and vector of the factor signals shall coincide. / Properties: / The amplification factors – are the vector of factors k_i the input value is multiplied by. / The initial conditions – are the vector of initial values y_i \( 0 \) for unit output values. / Note: by default the unit integrates the scalar input signal.