	First-order inertial element
in palette

in diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows: / T_i cdot {{d y}_i ( t )} over {d t} +y_i ( t ) =k_i cdot u_i ( t ) , / where u_i(t) is for the i-th element of input signal to the unit, T_i is for an element of constant time vector, k_{i italic " "} is an element of the amplification factors vector, y_i left ( t right ) italic " " is for an element of the unit output signal. / In case of zero initial conditions the dynamics of the unit can be represented via the following transfer function: / W \( s \) =k over {T cdot s + 1} (first-order aperiodicity), / that is why the pictogram of the unit has a view of the transfer function of first-order aperiodic circuit. / The dimensions of input, output and vector of the factors signals shall coincide. / Mandatory condition: T_i <> 0 . / Properties: / The amplification factors – are the vector of factors k_i the input value is multiplied by. / Time constants – are the vector of time constants T_i in seconds. / The initial conditions – are the vector of initial values y_i left ( 0 right ) for unit output value. / Note: by default the unit implements “the inertia” of the scalar input signal.