	Inertial-integrating element
in palette

in diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows: / T_i cdot y_i''(t) + y_i'(t) ~=~ k_i cdot x_i(t) , / where x_i(t) is for the i-th element of input signal to the unit, T_i is for the element of the vector of the time constants, k_i is for the element of the vector of the amplification factors, y_i(t) is for the element of the unit output signal. / In case of zero initial conditions the dynamics of the unit can be represented via the following transfer function: / W(s) =k over {s cdot (T cdot s + 1)} , / that is why the pictogram of the unit has the view of a transfer function of a inertial-integrating element. / The dimensions of input, output and vectors of the coefficients must be the same. / Mandatory condition: T_i <>0 . / Properties: / The amplification factors – the vector of the factors k_i the input value is multiplied by. / Time constants – the vector of time constants T_i in seconds. / Initial conditions – the vector of initial values y_i(0) for unit output value. / Initial conditions on the derivate – the vector of initial conditions for the unit output derivate y_i'(0) . / Note: by default the unit properties are set for the scalar input signal.