	Amplifier
in palette

in diagram
The unit is vectorized and multiplies (amplifies) the input value by a preset amplification factor in elementwise manner: / y_i(t) = k cdot u_{i}(t) , / where u_{i}(t) is for the i-th element of the input vector signal, y_i(t) is for the element of the output vector signal vec{y}(t) . / Output dimension is equal to the input dimension. / Properties: / The amplification factor - the scalar factor for the input value.