	Parabolic Function
in palette

in diagram
The unit is vectorized and implements the transformation of an input signal (a scalar or vector one) as per the formula: / y(t) = a_0 + a_1 cdot x(t) + a_2 cdot left ( x(t) right )^2 , / where a_0,~a_1,~a_2 are for the parabola coefficients, x(t),~y(t) are for input and output signals. / Properties: / Free member – the coefficient a_0 . / Coefficient at t – the coefficient a_1 . / Coefficient at t^2 – the coefficient a_2 . / The properties can be vectors, which dimensions shall be equal to the input dimension; in this case a vector will be at the output. / Note: by default this unit implements the quadratic transformation of an input (scalar or vector) signal with the properties a_0=0,~a_1=0,~a_2=1 .