	Polynomial Function
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y_i(t) = a_{1,i} + a_{2,i} cdot x_i(t) + a_{3,i} cdot left ( x_i(t) right )^2 + ...+a_{n,i} cdot left (x_i(t) right )^{n-1} , / where a_{1,i},~...,~ a_{n,i} are for the polynomial coefficients, x_i(t),~y_i(t) are for the input and output signals, i is for the number of the coefficient matrix line and the output vector element. / Property: / Polynomial coefficients are presented by the coefficient matrix a with polynomial coefficient values set in every line for a certain output vector element.