	Sinusoidal Function
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) = a cdot sin(%omega cdot x(t) + f) , / where a,~%omega,~f are for amplitude, circular frequency (rad/s) and phase (rad), / x(t),~y(t) are input and output signals. / If f=0 the unit implements the transformation “sine-wise”, and if f=%pi over 2 – “cosine-wise”. / Properties: / Amplitude – the coefficient a . / Frequency – the coefficient %omega . / Phase – the coefficient f . / The parameters can be vectors, which dimensions shall be equal to the input dimension; in this case there will be a vector at the output.