	Hyperbolic Function
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) = {k} over {%epsilon + x(t)} , / where k,~%epsilon for are amplification coefficient and “addition” to the denominator; are for x(t),~y(t) input and output signals. / Properties: / Numerator – the coefficient k . / Denominator minimum value – the coefficient %epsilon . / The properties can be vectors, which dimensions shall be equal to the input dimension; in this case there will be a vector at the output.