	AND Operator
in palette

in diagram
The unit is vectorized and implements the logical AND operation: / y(t) = left lbrace stack{ alignl 1, ~ if ~ u_1(t) = 1 ~"AND"~ u_2(t) = 1 ~ "AND" ~...~ "AND" ~ u_n(t) = 1; # alignl 0, ~ otherwise ~ (if ~ at ~ least ~ one ~ of ~ u_i(t) = 0); } right none , / where y(t) is for unit output signal, u_1(t),~u_2(t) are for input signals. / Properties: / Number of ports – the number of input ports n . / Notes: / In case an input signal is not logical one (0 or 1) but presents an integer signal then all non-zero signals will be considered by the unit as equal to one (True). There can only be either 0 or 1 at the unit output. / In “SimInTech” Software system the logical one (True) is equal to 1, the logical zero (False) is equal to 0.