	EQUAL-TO Operation
in palette

in diagram
The unit is vectorized and implements the EQUAL-TO logical operation: / y(t) = left lbrace stack{ alignl 1, ~ if u_1(t) = u_2(t); # alignl 0, ~ if u_1(t) <> u_2(t); } right none , / where y(t) is for unit output signal, u_1(t),~u_2(t) are for input signals. / Properties: / Second operand type – indicates the type of the second operand. In case it is a vector then elementwise operation is carried out. In case it is a scalar then operation with every element of the first input and the value of the second input is carried out.