	Linear with Saturation
in palette

in diagram
The unit is vectorized and implements the algorithm of a linear element with saturation: / y(t) = left lbrace stack{ alignl k cdot x(t), ~ if ~ a < x(t) < b # alignl y_1, ~ if ~ x(t) <= a # alignl y_2, ~ if ~ x(t) >= b} right none , / where x(t) is for the vector of input signals, y(t) is for the vector of output signals, k = {y_2 - y_1} over {b-a} . / Properties: / Argument lower limit – the property a . / Argument upper limit – the property b . / Function lower value – the property y_1 . / Function upper value – the property y_2 . / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.