	Linear with non-sensitivity zone
in palette

in diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of uniform non-linear static characteristic of “linear with non-sensitivity zone” type as per the following algorithm: / y(t) = left lbrace stack{ alignl k cdot (x(t)-a), ~ if ~ x(t) < a # alignl 0, ~ if ~ a <= x(t) <= b # alignl k cdot (x(t)-b), ~ if ~ x(t) > b} right none / where x(t) is for the vector of input signals, y(t) is for the vector of output signals, k is for the amplification coefficient. / Properties: / Argument lower limit – the property a . / Argument upper limit – the property b . / Amplification coefficient – the property k . / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.