	Relay multivalued (hysteresis)
in palette

in diagram
The unit is vectorized and implements the transformation of input signals by means of unified non-linear static characteristic of “relay multivalued” type with different initial conditions as per the following algorithm: / y(t) = left lbrace stack{ alignl y_1, ~ if ~ x(t) < a # alignl y(t - %DELTA t), ~ if ~ a <= x(t) <= b # alignl y_2, ~ if ~ x(t) > b} right none , / where x(t) is for the vector of input signals, y(t) is for the vector of output signals, %DELTA t is for the previous integration step, a,b,y_1,y_2 are for the parameters of static characteristics. / Properties: / Switch-over lower limit – a – the minimum input value whereby the output value is equal to the lower value. / Switch-over upper limit – b – the maximum input value whereby the output value is equal to the upper value. / Function lower value – y_1 – the minimum value at the unit output. / Function upper value – y_1 – the maximum value at the unit output. / Initial conditions (0;1) – the initial state of the relay: 0 – off, 1 – on. / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.