	Linear with saturation and non-sensitivity zone
in palette

in diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of unified non-linear static characteristic of “linear with saturation and non-sensitivity zone” type as per the following algorithm: / y(t) = left lbrace stack{ alignl y_1, ~ if ~ x(t) <= a_1 ; # alignl k_1 cdot (x(t)-a), ~ if a_1 < x(t) < a ; # alignl 0, ~ if ~ a <= x(t) <= b # alignl k_2 cdot (x(t)-b), ~ if ~ b < x(t) < b_1 ; # alignl y_2, ~ if ~ x(t) >= b_1 ; } right none , / where x(t) is the vector of input signals; y(t) is the vector of output signals; / k_1 = {y_1} over {a_1-a} ~ ; ~ k_2 = {y_2} over {b_1-b} ~ . / Properties: / Limitation lower limit – a_1 . / Non-sensitivity zone lower limit – a . / Non-sensitivity zone upper limit – b . / Limitation upper limit – b_1 . / Function lower value – y_1 . / Function upper value – y_2 . / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.