	Sign
in palette

in diagram
The unit is vectorized and implements the calculation of a sign for each element of the input vector value as per the following algorithm: / y_i(t) = left lbrace stack{ alignl -1, ~ if ~ u_i(t) < 0 ; # alignl 0, ~ if ~ u_i(t) = 0 ; # alignl +1, ~ if ~ u_i(t) > 0 ; } right none / where u_i(t),~y_i(t) are for the i-th elements of input and output vector signals. / Properties: any properties are not required for operation of the unit.