	Lower or Upper Limit
in palette

in diagram
The unit is vectorized, memorizes and delivers the extreme (minimum or maximum) value of input signal (or extreme values within the vector of input signals) to the output port as fixed in the process of simulation within the given time interval. / Algorithm of the unit for calculating the maximum: / y_i(t) = left lbrace stack{ alignl u_i(t), ~ if ~ u_i(t) > y_i(t-%DELTA t) # alignl y_i(t-%DELTA t), ~ if ~ u_i(t) <= y_i(t-%DELTA t) } right none . / Algorithm of the unit for calculating the minimum: / y_i(t) = left lbrace stack{ alignl u_i(t), ~ if ~ u_i(t) < y_i(t-%DELTA t) # alignl y_i(t-%DELTA t), ~ if ~ u_i(t) >= y_i(t-%DELTA t) } right none , / where u(t) is for the vector of input signals, y(t) is for the vector of output signals. / Properties: / Operation type – the calculation of the signal minimum or signal maximum. / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.