	Key-2
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y_1(t) = left lbrace stack{ alignl u(t), ~ if ~ u(t) <= K_1 # alignl y_10, ~ if ~ u(t) > K_1 } right none newline y_2(t) = left lbrace stack{ alignl u(t), ~ if ~ u(t) > K_2 # alignl y_20, ~ if ~ u(t) <= K_2 } right none , / where u(t) is for the vector of input signals; / y_1(t) is for the vector of signals at the 1st output port; / y_2(t) is for the vector of signals at the 2nd output port; / K_1, K_2 are for the vector of threshold values (settings) defining the conditions for overcommutation of signals at the unit output ports; / y_10 is for the vector of signals at the 1st output port of the unit with input signals featuring greater threshold values K_1 ; / y_20 is for the vector of signals at the 2nd output port of the unit with input signals featuring lesser threshold values {italic " " K}_2 . / Properties: / First output setting – the vector of threshold values K_1 . / Second output setting – the vector of threshold values K_2 . / 1st output initial value – the vector of signals y_01 at the 1st output port of the unit with input signals featuring greater threshold values K_1 . / 2nd output initial value – the vector of signals y_02 at the 2nd output port of the unit with input signals featuring lesser threshold values K_2 .