	Key-4(t)
in palette	| vectorized |

in diagram
The unit implements the function of controllable key as per the algorithm: / y_i(t) = left lbrace stack{ alignl Y_{0,i}, ~ "if" ~ t < T_{0,i}, # alignl u_i(t), ~ "if" ~ t >= T_{0,i}; } right none / where u(t) is for the vector of input signals; / y(t) is for the vector of output signals; / T_0 is for the vector of bridging times for corresponding inputs and outputs; / Y_0 is for the vector of unit output signals with times less than T_0 . / Properties: / Time setting – vector T_0 . / Subthreshold value at the output – vector Y_0 . / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.