	Key-7(t)
in palette	| vectorized |

in diagram
The unit implements the function of controllable key as per the algorithm: / y_i(t) = left lbrace stack{ alignl u_{1,i}(t), ~ "if" ~ t < T_{0,i}, # alignl u_{2,i}(t), ~ "if" ~ t >= T_{0,i}; } right none / where u_1(t),~u_2(t) are for vectors of signals at the 1st and 2nd input ports; / y(t) is for the vector of output signals; / T_0 is for the vector of time for re-switching inputs to the unit output. / Properties: / Setting values – vector T_0 . / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.