	Controllable key transferable over inputs type 1
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y(t) = left lbrace stack{ alignl x_1(t), ~ if ~ Control(t) = 0; # alignl x_2(t), ~ if ~ Control(t) = 1;} right none / where x_1(t), x_2(t) are for unit input signals (or vectors of signals), y(t) is for unit output signal (or vector of signals). / Control signal enters the unit from the top. In the process of calculation the image of the unit changes depending on the availability of a control signal: the key is normally transferred to the first input, when a control signal is delivered the key is transferred to the second input: / Control = 0 Control = 1 / The unit is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: any properties are not required for operation of the unit.