	Classic neutron kinetics model
in palette	| scalar |

in diagram
The unit implements classic neutron kinetics model, the differential equations of which have been obtained on the basis of known equations for “point” nuclear reactor kinetics in one-velocity approximation. / The unit has one input and one output signal. / This typical unit corresponds to constant (in terms of time) intensity of outer neutron source. / Input signal to the unit is absolute change in reactivity left ( %rho (t) - %rho (0) right ) . / Output signal from the unit is either dimensionless deviation of neutron power tilde {n}(t) = {N(t) - N(0)} over {N(0)} , or dimensionless neutron power tilde {n}(t) = {N(t)} over {N(0)} . / Properties: / Effective delayed neutron fraction. / Initial subcriticality (in fractions %beta_eff ). / Instantaneous neutrons lifetime, sec. / Number of delayed neutron groups. / Relative fractions of delayed neutron groups. / Decay constants for delayed neutron groups. / Normalizing (1 – if the unit output is normalized power; 0 – if the unit output is normalized power deviations) / Mathematical representation of this unit has been obtained on the basis of known equations for “point” nuclear reactor kinetics in one-velocity approximation. (i.e., nuclear fission process is ensured by neutrons of the same energy group: either only by slow or by fast ones): / left lbrace stack{ {dN(t)} over {dt} ~=~ {%rho(t) - %beta_эфф } over {l} cdot N(t) ~+~ sum from {i=1} to{6} {%lambda_i cdot C_i(t)} ~+~ S(t), # {dC_i(t)} over {dt} ~=~ {%beta_i } over {l} cdot N(t) ~-~ {%lambda_i cdot C_i(t)}; } right none / where {N(t)} is for the reactor power; / %rho (t) is for reactivity; / %beta_eff is for effective fraction of delayed neutrons; / l is for lifetime of instantaneous neutrons; / {C_i(t)} is for the i-th group delayed neutron core-precursor concentration; / %lambda_i is for decay constant of the i-th group core-precursors; / %beta_i is for fraction of the i-th group delayed neutrons; / S(t) is for intensity of neutron outer source. / Upon transformation, the initial system of equations appears as follows: / left lbrace stack{ {d tilde {n}(t)} over {dt} ~=~ {%beta_eff } over {l} cdot left [ - tilde {n}(t) cdot (1 + %rho_0^{%*%} ) ~+~ sum from {i=1} to{6} {%beta_i^{%*%} cdot tilde {c}_i(t)} ~+~ tilde {%rho}(t) cdot left ( 1 + tilde{n}(t) right ) right ] , # {d tilde {c_i}(t)} over {dt} ~=~ {%lambda_i } cdot left [ tilde {n}(t) ~-~ { tilde {c}_i(t)} right ] ; } right none / where tilde {c}_i(t) is for normalized deviation of the i-th group delayed neutron core-precursor concentration; / %rho_0^{%*%} is for absolute (in terms of module) nuclear reactor subcriticality in fractions %beta_eff ; / tilde {c}_i(t) is for reactivity relative change in fractions %beta_eff ; / %beta_i^{%*%} is for relative fraction of the i-th group delayed neutrons. / With t=0 the reactor is in stationary mode, thus, tilde {n}(t) = tilde {c}_i(t) = 0 . / Notes: / By default parameters, which approximately comply to RBMK-1000 reactor (High Power Channel-type Reactor) data, are entered in first lines. / By default %beta_i and %lambda_i comply to data for “pure” fuel U-235, though the User will be able to correct those, e.g., if in the process of reactor operation the nuclide fuel composition changes. / The structure of this unit dialog window allows another number of delayed neutron core-precursor groups to be set as well, and %beta_i and %lambda_i , correspondingly. For instance, if photoneutron share is considered, then number of groups can be increased, e.g., up to 8, and vice-verse - a single-group delayed neutrons kinetics model can be applied. / If reactor is subcritical then it is considered that its stationary condition with t<=0 has been ensured due to an external neutron source. / Transfer to the absolute nuclear reactor power, when using this unit, shall be conducted as per the formula: N(t) = N(0) cdot left [ 1 + tilde {n}(t) right ] , where N(0) is for stationary power value with t=0 .