	Quadratic objective
in palette	| vectorized |

in diagram
The unit implements the integral transformation: / y(t) = 1 over T cdot int from 0 to T {sum from {i=1} to n {[u_i(t) cdot a_i]^2} dt} / (quadratic objective), where / u_i(t) is for the i-th element of unit input signal, T = t is for current simulation time, a_i is for weight coefficients vector element, y(t) is for unit output signal. / Properties: / Weight coefficients – weight coefficients vector a or input vector elements. / Note: by default the unit implements the integral transformation of a scalar input signal with unitary weight coefficient: / y(t) = 1 over T cdot int from 0 to T {[u(t)]^2} dt / Variant of integral transformation for input vector with dimension 3: / y(t) = 1 over T cdot int from 0 to T { left ( [a_1 cdot u_1(t)]^2 + [a_2 cdot u_2(t)]^2 + [a_3 cdot u_3(t)]^2 right ) } dt