	TCP-IP Client
in palette	| vectorized |

in diagram
The unit executes bidirectional data exchange as per TCP-IP protocol. / Properties: / Number of inputs. / Output dimensions array. / Output initial values array. / Data exchange interval – an interval, in which data is recorded and read out in unit buffers. / Send stop command for server – if flag is set up then when calculation is stopped a stop command will be sent to Server. / Synchronize model time – if flag is set up then the unit will automatically perform delay of calculation for coordination of model time in Client and Server. / Tcp-ip port – exchange TCP-port No. / Server address – the IP-address or name of Server, wherein the model, the data have been exchanged with, is located.