	Multiplication of matrix on vector
in palette	| vectorized |

in diagram
The unit implements the procedure for multiplication of square matrix on vector of a correspondent dimension: / y(t) = A cdot u(t) ~=~ left [ stack{ alignl a_11~ a_12 ~...~ a_1n # alignl a_21~ a_22 ~...~ a_2n # alignl . . . . . . . . . . . . . . . . . . # alignl a_n1~ a_n2 ~...~ a_nn } right ] ~cdot~ [u_1(t),~u_2(t),...~u_n(t) ] , / where A is for matrix of coefficients; x(t) is for vector of solutions; u(t) is for vector of right parts, y(t) is for vector at the unit output. / The unit has two vectorized input ports: / 1st input port – for entering the matrix A represented as a vector of coefficients, when unpacking the matrix in linewise manner. / 2nd input port – for entering the vector u(t) . / The unit has one vector output port intended for outputting the vector y(t) . / Vector signal dimension at the 1st input port shall be equal to n times n , where n is for the matrix dimension (number of equations in the system), while dimensions of 2nd input port and output port signals are the same and equal to n . / Properties: / Matrix dimension – natural number n equal to the number of matrix lines (or columns). / Example. / It is needed to multiply the matrix A on the vector u if: / A = left [ stack{ 2 , ~~~3 # 5 ,~- 2 } right ] ;~ u = left [ stack{ 8 # 1 } right ] ; / and the result of multiplication is obvious: vector-column, elements of which are 19 and 38. / The figure below demonstrates a block diagram for this task solution. Typical Replicator units are used for generating input vector signals: / Note: the unit carries out the procedure for multiplication of square matrix on vector after every successful completion of an integration step. / Solutions