	1st-order analytic aperiodicity
In pallette

In diagram
The unit is vectorized and implements the analytic-discrete mathematical model for 1st-order aperiodic element, the continuous mathematical model of which dynamics is described via a linear ordinary differential equation (ODE) featuring the next appearance: / T_i cdot {{dy_i(t)}over{dt}} + y_i(t) = k_i cdot u_i(t) , / where u_i(t) is for the i-the element of input signal to the unit, T_i is for the vector of time constants, k_i is for the vector of amplification coefficient, y_i(t) is for element of output signal from the unit.. / Mandatory condition: T_i <> 0 / The algorithm of the unit realizes the calculation of output signal to discrete moments of time (at every step of integration including a bad one) as per the following relation: / y_{j+1} = k cdot u_{j+1} + (y_j - k cdot u_{j+1}) cdot exp(- {{%DELTA t_{j+1}} over {T}} ) , / where y_j is for the value of signal at the unit output at j-th step of integration, x_{j+1} is for the value of signal at the unit input at (j+1)-th step of integration, %DELTA t_{j+1} is for the current step of integration. / Properties: / Amplification coefficients - vector of the coefficients k_i the input value is multiplied by. / Time constants - vector of time constants T_i given is seconds. / Initial conditions - vector of initial conditions y_i(0) of unit output value. / Additional inputs – is to indicate the availability of additional inputs in the unit. / Initial conditions are given from - is to indicate the source of the unit initial conditions. / If option “Input translation attribute” is selected in 4-th dialog line a new additional input port appears next to the unit to enter a logic control signal to the unit, where 0 corresponds to the input signal transformation as per the basic algorithm (see the formula), while 1 corresponds to the momentary transmission of input signal to the unit output (without transformation). / If option “Time constants through ports” is selected in 4-th dialog line a new additional input port (second or third) appears in the unit to enter the element time constants to the unit. This, for example, allows the element time constants to be dynamically changed in the process of simulation. / If an option from “Unit parameters” is selected in the 5-th dialog line then the initial condition is to be picked up from the 3-rd dialog line. / If “Input” option (default value) is selected in the 5-th dialog line then the initial condition is picked up from the 1-st input port at the zero calculation step (“at start”).