	Store value of signals
in palette	| vectorized |

in diagram
The unit stores a signal (signals) as per the following algorithm: / If ~ u_{2,i}(t) > 0 ~ then ~ y_i(t) = u_{1,i}(t) ~ otherwise ~ y_i(t) = y_i(t - %DELTA t) , / where u_{1,i}(t), ~ u_{2,i}(t) are for the i-th elements of the first and second vector input signals,is y_{i}(t) for the i-th element of vector output signal. / In other words, if a non-zero signal is delivered to the second input the signal value at the output will be equal to the signal value at the first input. / In case of a zero signal at the second input the unit “memorizes” the first input value and then the output will not change (till the next regular moment of time when a positive signal again is delivered to the second input). / Properties: no properties are required for operation of the unit.