	One of many
In palette

In diagram
The unit is vectorized and implements the special algorithm for generation of logic signals in the output vector depending on a change of a type of logic signal in the input vector. / Algorithm of operation of the unit: / Before the commencement of simulation process only one signal (e.g., N-th) in the output vector in the unit dialog window can be set as TRUE type signal (active) regardless of the type of relevant (N-th) signal in the input vector. All other output signals will be considered as FALSE type signals (non-active) regardless of the type of relevant signals in the input vector. / If any logic signal (any except for N-th) in the input vector changes its type from FALSE to TRUE in the process of simulation then a relevant signal in the output vector will change its type to TRUE (active) and N-th signal in the output vector will turn into FALSE (non-active). / Properties: any properties shall not be set for operation of the unit.