	One of many, optional
In palette

In diagram
The unit implements the special algorithm for generation of the vector of output logic signals depending on the value of input scalar signal rounded to the whole number. / Algorithm of operation of the unit: / If in the process of simulation the scalar intput signal, when rounded up to a whole number, is equal to M( 1 <= M <= N , where N is dimensionality of the output vector) then in the output vector only M -th signal features the TRUE type (active), while all other signals in the output vector correspond to the FALSE type (non-active). / If the value of input scalar signal rounded up to a whole number is less than 1 or more than N then all signals in the output vector will correspond to the FALSE type. / Property: / Dimensions of every vector – it is dimensionality of unit output and input signals.