	Integral part
in palette	| vectorized |

in diagram
The unit implements the operation of separation of the integral part of an input signal. / The integral part is understood as a nearest integer rounded down (in terms of absolute value). I. e., the integral part of a positive number is less than or equal to the number, while the integral part of a negative number is more than or equal to the number (see the Figure): / Integral part calculation algorithm: / y(t) = left lbrace stack{ "int" left [ u(t) right ] ~=~ max left ( {n in Z} ~divides~ {n <= u(t)} right ) , ~ with ~u(t) >=0 # "int" left [ u(t) right ] ~=~ min left ( {n in Z} ~divides~ {n >= u(t)} right ) , ~ with ~u(t) <0 } right none , / where y(t) is for output signal, u(t) is for unit input signal, Z is for set of integers. / In case of a vector input signal the unit implements the operation of separation of the integral part for each element of the input vector value. / Properties: no properties are required for operation of the unit. Note: output signal dimension is always equal to the input signal dimension. / Integral part of linear function / Time, t (s)