	Extrapolator
In palette

In diagram
The unit is vectorized and implements the zero-order extrapolation: / y(t) = u(t[k]) , / where y(t) is for the value of an output signal at a current moment of calculated (simulated) time, u(t[k]) is for the value of input signal at the last moment of discretization t[k] . Discretization takes place with period T , which is set by a unit parameter. / Note: / To ensure correct operation of the unit one shall set the minimum step of integration not more than 0.5 cdot T . / During integration with constant step the step is recommended to be set so that the sampling period would be equal to the step of integration T = k cdot h , where k,~h is for the whole number and step of integration. / Properties: / Sampling period – is sampling period for unit calculation.