	Sampling time delay
in palette	| vectorized |

in diagram
The unit implements the input signal discrete delay by one sampling period: / y(t) = u(t[k-1]) , / where y(t) is for output signal value at the current moment of estimated (simulation) time,is u(t[k-1]) for input signal value at the next-to-last discretization moment t[k-1] . The sampling runs with the period of T , which is set by the unit parameter. / Note: / To ensure the correct operation of the unit the maximum step of integration shall be set up not higher than 0.5 cdot T . In case the integration runs with a constant step, the step is recommended to be set up so that the sampling period would be multiple to the step of integration T = k cdot h , where k,~h are for the integer number and for the step of integration. / Properties: / Sampling period – unit calculation sampling period / Initial conditions – output value with t = 0 .