	General sampled data transfer function
in palette	| vectorized |

in diagram
The unit implements a mathematical representation of a circuit, the dynamics of which (for every scalar signal) can be described via the sampled data transfer function: / W(z) ~=~ {b_m cdot z^m +...+ b_2 cdot z^2 + b_1 cdot z + b_0} over {a_n cdot z^n +...+ a_2 cdot z^2 + a_1 cdot z + a_0} , / where a_i,~b_j are for coefficients ( i=0...n,~j=0...m,~n>=m ). / Mandatory conditions: m <= n,~a_n<>0. / Notes: / By default the unit implements the processing of a scalar input signal. / Coefficients a_i,~b_j are introduced in ascending powers z. / To ensure the correct operation of the unit the maximum step of integration shall be set up not higher than T/2 . In case the integration runs with a constant step, the step is recommended to be set up so that the sampling period would be multiple to the step of integration T = k cdot h , where k,~h are for the integer number and for the step of integration. / Properties: / Sampling period – T . / Numerator coefficients – vector b with dimension [m]. / Denominator coefficients – vector a with dimension [n]. / Initial conditions – vector of initial values for the unit output with t=0.