	Discrete PID controller
in palette	| vectorized |

in diagram
The unit implements the data transfer function for discrete PID controller: / W(z) = K_P + K_I cdot {{T cdot z} over {z-1}} + K_D cdot {{z - 1} over {T cdot z}} , / where K_P,~K_I,~K_D are for proportional, integral and differential components; T is for sampling period. / Note: To ensure the correct operation of the unit the maximum step of integration shall be set up not higher than T/2 . In case the integration runs with a constant step, the step is recommended to be set up so that the sampling period would be multiple to the step of integration T = k cdot h , where k,~h are for the integer number and for the step of integration. / Properties: / Sampling period – unit calculation sampling period T . / Initial conditions – vector of initial values y_i(0) for the unit output. / Proportional component – K_P . / Integral component – K_I . / Differential component – K_D .