	Discrete derivate
in palette	| vectorized |

in diagram
The unit implements a numerical determination for derivate as per the formula: / y_i(t) ~=~ {u_i(t[k])~-~u_i(t[k-1])} over {t[k]~-~t[k-1]} / where u_i(t[k]),~u_i(t[k-1]) are for values of the i-th element of unit input signal at the last and next-to-last moments of discretization t[k],~t[k-1] ; / y_i(t) is for the i-th element of the unit output signal at a current moment of simulation time. / Notes: / By default the unit implements the calculation of a discrete derivate for scalar input signal. / To ensure the correct operation of the unit the maximum step of integration shall be set up not higher than T/2 . In case the integration runs with a constant step, the step is recommended to be set up so that the sampling period would be multiple to the step of integration T = k cdot h , where k,~h is for the integer number and for the step of integration. / Properties: / Sampling period – unit calculation sampling period T . / Initial conditions – vector of initial values y_i(0) for unit output.