	Zero order difference
in palette	| vectorized |

in diagram
The unit is vectorized and implements the calculation of 0-order difference as per the formula: / y_i(t) ~=~ {u_i(t)~-~u_i(t- %DELTA t)} / where u_i(t),~u_i(t - %DELTA t) are for values of the i-th element of unit input signal at the current and previous steps of integration; / y_i(t) is for the i-th element of unit output signal at a current moment of simulation time. / Notes: / By default the unit implements the calculation of 0-order difference for scalar input signal. / Properties: / Initial conditions – vector of initial values y_i(0) for unit output. / Algebraic loop solution – a flag indicating whether this unit should solve algebraic loops.