	Distribution histogram
in palette	| scalar |

in diagram
This unit is intended to plot the frequency function of signal distribution (histogram). / The calculation algorithm for the frequency function is as follows: / First, minimum and maximum values x_min ~ "and" ~ x_max of a random signal are calculated. / The whole interval left [ x_min, ~ x_max right ] is divided into a preset number of intervals m, wherein limits of each interval are calculated as per the formulas: / alignl L_i ~=~ x_min ~+~ (i-1) cdot h , newline alignl R_i ~=~ x_min ~+~~ i cdot h, / where L is for the left limit of the i-th interval; R is for the right limit of the i-th interval. Interval width: / h ~=~ {x_max - x_min} over {N} / Then a number of times the value falls within the i-th interval N_i is calculated. / Frequency function in the i-th interval is estimated as per the formula: p_i ~=~ {N_i} over {n cdot h} , where n is for sampling range. / The unit has 1 input and 2 output ports. / Input signal shall be scalar. / Signal at the 1st output port is vector of class marks of histogram intervals. / Signal at the 2nd output port is vector of histogram values. / The outputs are of the same dimension, which complies with the Number of Intervals property. / Properties: / Size of series – value of this property determines the size of series in sampling. / Calculation over the whole sampling (Yes or No) – if this property is Yes then the frequency function will be calculated over the whole sampling and averaged. If the property is No then the frequency function will be calculated over separate series. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero) then the read-out is running with the period equal to the step of integration. / Linear trend (Yes or No) delete – if this property is Yes, then linear trend is preliminarily subtracted from the array of accumulated input signal values. / Lower limit – the value of this property determines the left limit position, when plotting the histogram. / Upper limit - the value of this property determines the right limit position, when plotting the histogram. / Number of intervals – the value of this property determines the number of partition intervals m, when plotting a frequency function graph. / Calculate limits automatically (Yes or No) – if this property is Yes then limits of histogram intervals will be automatically calculated as per the first series, and the limits of the intervals will not be further changed. If this property is No then the limits of the intervals will be calculated as per the Lower Limit and Upper Limit properties. / Displayed value (Relative number for falling within, Absolute number for falling within, Absolute frequency function, Relative frequency function) – name of options determines a type of a histogram to be calculated. / If Absolute number for falling within option is selected then the number of values N_i , fallen within the i-th interval, will be displayed. / If Relative number for falling within option is selected then relation of the number of values N_i , fallen within the i-th interval, towards sampling size N is displayed. / If Absolute frequency function option is selected then empiric frequency function value {N_i} over {N cdot h} is displayed, where h is for histogram interval width. / If option Normalized frequency function is selected then a mean value is subtracted from the initial signal, i.e. the relation of interval class mark coordinate to mean-square deviation – at the first output port, and the product of absolute frequency function by mean-square deviation – at the second output port.