	Arithmetic average
in palette	| vectorized |

in diagram
The unit implements the calculation for input signal arithmetic average. The arithmetical average value is calculated as per the formula: / overline {x} ~=~ {{1} over {N}} cdot sum from{i=1} to{N} {x_i } / where N is for the sampling volume (a number of values), / x_i is for values of the i-th element of sampling. / The unit has 1 input port and 1 output port. Input signal can be vector. Dimension of output signal is always equal to dimension of input signal. / Properties: / Size of series – value N of this property determines the size of series in sampling. / Calculation over the whole sampling (Yes or No) – if this property is No, then the average value will be calculated by separate series. If this property is Yes, then the average value will be specified immediately after receiving the next new signal value at the unit input. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration.