	Mean-square deviation
in palette	| vectorized |

in diagram
The unit implements the calculation of mean-square deviation for input signal. / Mean-square deviation is calculated as per the following formula: / %sigma ~=~ sqrt{ {{1} over {N-1}} cdot sum from{i=1} to{N} {left ( x_i-M right )^2 }} / where N is for the sampling volume (a number of values), / x_i is for values of the i-th element of sampling, / M is for mathematical expectation of random value. / This value describes the strength of oscillating component of a signal. Value equal to mean-square deviation is referred to as dispersion. / The unit has 1 input port and 1 output port. Input signal can be vector. Dimension of output signal is always equal to dimension of input signal. / Properties: / Size of series – value N of this property determines the size of series in sampling. / Calculation over the whole sampling (Yes or No) – if this property is No, then the mean-square deviation will be calculated by separate series. If this property is Yes, then the mean-square deviation will be specified immediately after receiving the next new signal value at the unit input. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration. / Delete linear trend (Yes or No) – if this property is Yes, then linear trend will be preliminarily subtracted from the array of accumulated input signal values.