	Spectral density
in palette	| scalar |

in diagram
The unit implements the calculation of spectral density for scalar input signal. / Spectral density is calculated as per the following algorithm: / The implementation is divided into separate series; the size of series shall be an integral power of 2. / Data is preliminarily prepared, which includes deletion of average value or linear trend from initial data, multiplication of data by weight coefficients (time window). Multiplication of data by the time window allows errors related to the calculation of discrete Fourier transformation to be reduced, e.g., it reduces leakages through lateral maximums. / Fast Fourier transformation (FFT) method is used to calculate discrete Fourier transformation for sequence defined as per the formula: / X(f,T) = %DELTA t left ( sum from {n=1} to {N-1} {x_n cdot e ^ {{-i cdot 2 %pi f n} over {N}}} right ) / Absolute spectral density is determined as per the formula: %epsilon_k = {2 cdot %DELTA t} over { N cdot %zeta } cdot X_k , where %DELTA t is for signal sampling period; %zeta is for a coefficient dependent on a way the input value is weighed up; X_k is for discrete Fourier transformation value at the k-th harmonic curve. / Normalized spectral density is calculated by dividing the absolute one by signal dispersion. / The unit has 1 input port and 2 output ports. / Input signal shall be scalar. / Signal at the 1st output port is vector of frequencies. / Signal at the 2nd output port is vector of spectral density values. / Dimensions of signal outputs are the same and equal to N over 2 - 1 , where N is for size of series. / Properties: / Size of series – value of this property determines the size of series in sampling. The size of series shall be an integral power of 2. / Calculation over the whole sampling (Yes or No) – if this property is No, then the spectral density will be calculated by separate series. If the property is Yes, then the spectral density will be calculated against an unlimited number of values; results of the calculation will be averaged for all series. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration. / Delete linear trend (Yes or No) – if this property is Yes, then linear trend will be preliminarily subtracted from the array of accumulated input signal values. / Window type (Rectangular, Hanna, Welch, Parzen). Window type represents a method of calculation for weight coefficients along with preliminary data processing. If window type is Rectangular, then weight coefficients are equal to one. / Output (Absolute Spectrum, Normalized Spectrum). Option name determines the type of spectral density calculated by the unit. If Absolute Spectrum option is selected, then absolute spectral density of analyzed signal is displayed. If Normalized Spectrum option is selected, then normalized (for dispersion) spectral density of analyzed signal is displayed.