	Cross-spectral density
in palette	| scalar |

in diagram
The unit implements the calculation of cross-spectral density for two scalar input signals. / Cross-spectral density is calculated as per the following algorithm: / Implementation of two signals is divided into separate series; moreover, the size of series shall be an integral power of 2. / Data is preliminarily prepared, which includes deletion of average value or linear trend from initial data, multiplication of data by weight coefficients (time window). Multiplication of data by the time window allows errors related to the calculation of discrete Fourier transformation to be reduced, e. g., it reduces leakages through lateral maximums. / Fast Fourier transformation (FFT) method is used to calculate discrete Fourier transformation for two valid sequences: / X(f,T) = %DELTA t left ( sum from {n=1} to {N-1} {x_n cdot e ^ {{-i cdot 2 %pi f n} over {N}}} right ) , newline Y(f,T) = %DELTA t left ( sum from {n=1} to {N-1} {y_n cdot e ^ {{-i cdot 2 %pi f n} over {N}}} right ) . / Absolute cross-spectrum density is calculated as per the following formula: / G_xy = {2 cdot %DELTA t cdot X_i cdot Y_i} over { N cdot %zeta } , where %DELTA t is for signal sampling period; %zeta is for a coefficient dependent on a way the input value is weighed up. / Cross-spectrum density is normalized by dividing the absolute one by the value: %sigma_xy ^ 2 = sqrt {%sigma_x ^ 2 + %sigma_y ^ 2} , where %sigma_x ^ 2 is for dispersion of value x, %sigma_y ^ 2 is for dispersion of value у. / The unit has 2 input ports and 2 output ports. / Input signals shall be scalar. / Signal at the 1st output port is vector of frequencies. / Signal at the 2nd output port is vector of spectral density values. / Dimensions of signal outputs are the same and equal to N over 2 - 1 , where N is for size of series. / Properties: / Size of series – value of this property determines the size of series in sampling. The size of series shall be an integral power of 2. / Calculation over the whole sampling (Yes or No) – if this property is No, then the cross-spectral density will be calculated by separate series. If the property is Yes, then the cross-spectral density will be calculated against an unlimited number of values; results of the calculation will be averaged for all series. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration. / Delete linear trend (Yes or No) – if this property is Yes, then linear trends will be preliminarily subtracted from the array of accumulated input signal values. / Window type (Rectangular, Hanna, Welch, Parzen). Window type represents a method of calculation for weight coefficients along with preliminary data processing. If window type is Rectangular, then weight coefficients are equal to one. / Output (Absolute Spectrum, Normalized Spectrum, Phase Displacement Angle). Option name determines the type of spectral density calculated by the unit. If Absolute Spectrum option is selected, then absolute spectral density is displayed. If Normalized Spectrum option is selected, then normalized spectral density is displayed (normalized for the square root from a product of analyzed signals dispersion). If Phase Displacement Angle option is selected, then phase displacement value calculated as per the following formula will be displayed: / %phi = arctg left ( {Im(G_xy)} over {Re(G_xy)} right ) = arctg left ( {"Im"(G_xy)} over {"Re"(G_xy)} right )