	Multilink manipulator
in palette	| scalar |

in diagram
The unit implements a mathematical representation of manipulator on the basis of the Lagrange equation of the second kind. The manipulator is considered as a system of solid bodies interconnected via kinematic pairs of the fifth class (with rotational and translational joints), which represents an open kinematic chain. The first link via a kinematic pair of the fifth class is connected to a fixed rack. The last N-th link is a gripper. The manipulator links are numbered in sequence: 1, 2, …, N. Each link features an own system of coordinates ОiXiYiZi , while fixed system of coordinates О0X0Y0Z0 is connected to the base. For generation of motion equations the Denavit-Hartenberg system of coordinates is used. / The unit has the following input and output signals: / The following signals are delivered to the unit input ports: / Moments in links for rotational joints (forces for translational ones). / Force applied in a certain point. / Torque applied on the last link (in the projection on the axes of the system of coordinates О0X0Y0Z0). / The following signals are generated at the unit output ports: / Positions in joints (generalized coordinates of links). / Velocities in joints (generalized velocities of links). / Properties: / Number of chain links N. / Types of kinematic pairs of links (0 — rotational, 1 — translational). / Initial values of coordinates (Qi [rad]* — for rotational, Di [m] — for translational). / Initial values of velocities (d Qi/dt[rad/s] — for rotational, dDi/dt[m/s] — for translational). / Properties Ai [m]. / Property Alphai [rad]. / Di [m] – for rotational, Qi [rad] – for translational. / Moments of inertia for each link: / Jxxi [kg/m2] (against the plain YiOiZi ). / Jyyi [kg/m2] (against the plain XiOiZi ). / Jzzi [kg/m2] (against the plain XiOiYi ). / Centrifugal moment of inertia for each link: / Jxzi [kg/m2]. / Jyzi [kg/m2]. / Jxyi [kg/m2]. / Static moments for each link: / Sxi [kg/m]. / Syi [kg/m]. / Szi [kg/m]. / Weights of links Mi [kg]. / Orientation of vector g in the basic system of coordinates [x,y,z]. / * Parameters Ai, Alphai, Qi, Di are determined as per the following algorithm. / Algorithm for selection of a system of coordinates and for determination of parameters Ai, Alphai, Qi, Di. / To determine the parameters in the Denavit-Hartenberg system of coordinates proceed as follows: / Determine the basic coordinates [X0 Y0 Z0] so that axis Z0 would coincide with the first joint axis. / Direct all axes Zi along translational movement or rotational axes of the i-th link against the (i-1)-th link. / Set up the datum point of the i-th system of coordinates in cross point of axis Zi with common normal line to axes Zi and Zi-l. / Set up axes Xi in every i-th joint along the common normal line to axes Zi-1 and Zi. / Set up axes Yi, so that right threes of coordinates would be generated. / Find Di as a distance from the datum point of coordinates of the (i-1)-th system of coordinates to the cross point of axes Zi-l and Xi measured in the direction of axis Zi-l. If the i-th joint is translational then Di is a generalized coordinate. / Find Ai as a distance from the datum point of the (i-1)-th system of coordinates to the cross point of axes Zi and Xi, measured in the direction of axis Xi. / Find Qi as a rotation angle from axis Xi-l to axis Xi around axis Zi-l. / Find Alphai as a rotation angle from axis Zi-l to axis Zi against axis Xi. / Examples of filling in the dialog window: / Figure 1 represents the diagram of three-link manipulator. / Figure 1 / N of link/Property 1 2 3 / Length, m 1 0.8 1.6 / Weight, kg 50 20 10 / Moment of inertia Jxx, kg/m2 0 0 0 / Moment of inertia Jyy, kg/m2 16.7 4.27 0 / Moment of inertia Jzz, kg/m2 0 0 8.53 / Moment of inertia Jxz, kg/m2 0 0 0 / Moment of inertia Jyz, kg/m2 0 0 0 / Moment of inertia Jxy, kg/m2 0 0 0 / Static moment Sx, kg/m 0 0 0 / Static moment Sy, kg/m 25 8 0 / Static moment Sz, kg/m 0 0 -8 / Property A 0 0 0 / Property D 1 D2 D3 / Property Q Q1 0 0 / Property Alpha -pi/2 -pi/2 0 / D2, D3 and Q1 are generalized coordinates. / Vector g is directed downward in parallel to axis Z0. Initial velocities are equal to 0. Reference coordinates are equal to 1.57 rad, 0.2 m, 0 m, correspondingly.