	Interpolation
in palette	| vectorized |

in diagram
The unit is intended to interpolate table functions. The unit has three vector inputs and one vector output. Array of values of arguments of table functions with dimension N_pnt is applied to the first input. Array of values of table functions with dimension N_pnt times N_fun is applied to the second input (thus, interpolation of several functions set up in the same points against an independent argument can run simultaneously). Array of points of arguments with dimension N_arg is applied to the third input for interpolated function values to be calculated in those. Value N_arg is determined via input signal dimension. / Function values calculated after interpolation for the points set up at the third input port are applied to the unit output. Dimension of this output is equal to N_arg times N_fun . / Interpolation methods are implemented by Lagrange polynomials cubic splines. Interpolation order ( Order ) and index of interpolation start ( Idn ) are important only for interpolation by Lagrange polynomials. Values Order and Idn determine interpolation and extrapolation areas. Inside the [x(Idn),~x(Idn+Order)] interval a function is interpolated, outside this interval it is extrapolated. In case of interpolation by splines, the condition of equation to 0 for second derivates is set up at the interval boundaries. / Properties: / Interpolation method – Lagrange polynomial; Cubic spline; Linear. / Interpolation order – Order (for interpolation by Lagrange polynomials). / Number of function points – natural number N_pnt . / Index of interpolation start – natural number Idn (for interpolation by Lagrange polynomials). / Number of functions – natural number N_fun .