	Integral of table function
in palette	| vectorized |

in diagram
The unit is vectorized and implements the calculation of integrals of table functions following the trapezium method: / y(t) = int from{x_min} to{x_max} {u(x)}dx , / where x is for independent variable vector; x_min,~x_max are for minimum and maximum values of independent variable, correspondingly; u(x) is for numerical vector of function values. / Properties: / Number of function points – natural number n_point >=2 defines the number of points against an independent argument, and the dimension of the first input signal. / Number of functions – natural number n_fun>=1 sets up the number of functions and, together with the number of points, defines the dimension of the second input signal. The dimension of output signal is equal to n_fun . / The unit has two inputs and one output. The array of values of arguments of table functions with dimension n_point is applied to the first input. / The array of values of table functions with dimension left [ n_point times n_fun right ] is applied to the second input (thus, integral of several functions set up in the same points against independent argument x can be simultaneously calculated). / Values of integral of functions are applied to the unit output. The dimension of this output is equal to N_fun . / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Number of function points 20 / Number of functions 2 / Named definition of properties: / Name Value / Number of function points [np] / Number of functions [nf] / Notes: / The dimension of output signal is always equal to the number of functions. The unit generates a scalar output signal with n_fun =1 . / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.